Survey of Agata Beamline Equipment at GSI

Author: 		Survey Manager:	John Strachan

# 1. Introduction

This report is a compilation of a number of survey reports completed at GSI, and so is a summary of all the work undertaken. The report will identify all the components measured, starting from the furthest upstream component and working downstream. Section 2 gives descriptions of the items measured and section 3 contains the measured results in a table.

# 2.1. Description of Upstream Beamline.

This information is based on report: 186 Agata-ph2-meng-rep-0003v1

Names of Components.

Axis shown, Y is +ve along the beam direction.

Z is +ve in the vertical

All values given to the centre of the components.

These components are green in the results table in section 3.

# 2.2. Description of Hector Detectors.

The Hector Array are the 6 backward facing detectors. These are identified as shown in the image below and left. The Labr detectors are scarlett red, the CsI detectors are black.

Measurements and results are as described in report survey-agata-rep-006 iss01 results from this array are in blue. Two co-ordinates are given for each detector; the location of each detector front face with respect to the target co-ordinate frame and a point 100mm along the axis of the detector further away from the target point. These are called _0 and _100 respectively.

# 2.3. Description of Miniball and forward Labr crystals.

The miniball array are the 8 detectors angled at approximately 90 degrees to the target. They are named as shown below.

The forward LaBr detectors are the 4 detectors angled at approximately 112 degrees to the target. I have named them as shown below.

Measurements and results are as described in report survey-agata-rep-007 iss01 results from this array are in magneta. Two co-ordinates are given for each detector; the location of each detector front face with respect to the target co-ordinate frame and a point 100mm along the axis of the detector further away from the target point. These are called _0 and _100 respectively.

# 2.4. Description of Agata crystals.

This information is unique to this report. The crystals are assumed to be perfectly positioned within the array, and there co-ordinates are given relative to the measured position of the array.

Two points are give per crystal Point 1 is on the centre of the crystal at the crystal face, point 0 is 121.9mm away from the face along the cylinder axis. Points are named after the crystal colour.

Germanium Cryostats are named as listed above.

Eg crystal 01r1 is Cryostat1 red crystal on the face.

These components are red in the results table in section 3

# 3. Results table.

| Component | X Value | Y value | Z Value |
| --- | --- | --- | --- |
| magnet |  | -4160.5 |  |
| Tcp5 |  | -3970 |  |
| Downstream det |  | -3499 |  |
| Upstream det |  | -2848 |  |
| Tpc3 |  | -2540.5 |  |
| Vcollimator |  |  | 3.3 |
| Hcollimator | 1.4 | -2078 |  |
| Absorber |  | -1832.75 | 1 |
| vertfoil |  | -1593 |  |
| Window |  | -1382.3 |  |
| Lead Wall |  | -990 |  |
| BaFDET3_0 | 200.927 | -279.523 | -82.129 |
| BaFDET3_100 | 257.535 | -358.401 | -106.080 |
| BaFDET2_0 | 201.308 | -279.166 | 83.433 |
| BaFDET2_100 | 258.187 | -357.770 | 107.656 |
| LabrDET10_0 | 85.155 | -283.099 | 201.913 |
| LabrDET10_100 | 109.172 | -361.561 | 259.069 |
| LabrDET9_0 | -82.801 | -283.437 | 202.391 |
| LabrDET9_100 | -106.219 | -362.086 | 259.540 |
| BaFDET1_0 | -198.016 | -281.178 | 83.575 |
| BaFDET1_100 | -255.009 | -359.901 | 107.119 |
| BaFDET4_0 | 199.040 | -280.606 | -80.591 |
| BaFDET4_100 | -255.789 | -359.549 | -103.989 |
| LabrDET8_0 | 244.90 | -37.83 | -256.35 |
| LabrDET8_100 | 314.43 | -47.92 | -327.51 |
| LabrDET7_0 | 334.96 | -37.86 | -103.83 |
| LabrDET7_100 | 427.79 | -45.86 | -134.54 |
| BaFDET7_0 | 333.60 | -39.53 | 65.13 |
| BaFDET7_100 | 431.70 | -48.47 | 82.31 |
| BaFDET6_0 | 267.16 | -40.01 | 214.83 |
| BaFDET6_100 | 345.81 | -48.68 | 275.99 |
| BaFDET5_0 | -264.13 | -48.47 | 211.47 |
| BaFDET5_100 | -341.74 | -56.13 | 274.08 |
| BaFDET8_0 | -335.47 | -43.13 | 63.84 |
| BaFDET8_100 | -433.44 | -51.69 | 81.92 |
| LabrDET6_0 | -342.37 | -39.95 | -106.12 |
| LabrDET6_100 | -437.31 | -48.12 | -136.46 |
| LabrDET5_0 | -255.03 | -41.89 | -260.70 |
| LabrDET5_100 | -325.82 | -52.17 | -330.59 |
| Theoretical Target | 0 | 0 | 0 |
| Target vessel Centre | 1.33 | 1.72 | 0.83 |
| Vertical Target position | 3.165 | -0.864 |  |
| Rotary Target position |  | 142.7 | 2.488 |
| Agata array target | 3.6 | -2.9 | -2.7 |
| LabrDET4_0 | 317.07 | 146.08 | 168.89 |
| LabrDET4_100 | 397.74 | 183.96 | 214.14 |
| LabrDET3_0 | 229.53 | 146.05 | 272.04 |
| LabrDET3_100 | 287.36 | 184.08 | 344.21 |
| LabrDET2_0 | -249.81 | 147.56 | 248.47 |
| LabrDET2_100 | -316.55 | 187.08 | 311.58 |
| LabrDET1_0 | -328.7 | 143.07 | 138.31 |
| LabrDET1_100 | -414.31 | 187.32 | 173.06 |
| 01b0 | -74.223377 | 319.949977 | 124.768839 |
| 01b1 | -46.726619 | 209.695938 | 80.637385 |
| 01g0 | 13.411801 | 307.899627 | 170.05776 |
| 01g1 | 9.696584 | 201.862455 | 110.041717 |
| 02b0 | -140.583201 | 320.388603 | -37.716452 |
| 02b1 | -90.482751 | 209.982768 | -25.063136 |
| 02g0 | -156.614245 | 308.51514 | 59.639844 |
| 02g1 | -101.037871 | 202.264047 | 37.694865 |
| 03b0 | -6.556839 | 320.236367 | -151.039879 |
| 03b1 | -3.476981 | 209.885124 | -99.34145 |
| 03g0 | -104.141015 | 308.707224 | -136.18629 |
| 03g1 | -66.450438 | 202.388322 | -89.976751 |
| 04b0 | 142.635832 | 319.703653 | -58.592319 |
| 04b1 | 94.051675 | 209.537947 | -39.547451 |
| 04g0 | 98.31527 | 308.210426 | -146.795581 |
| 04g1 | 65.660227 | 202.063536 | -96.535298 |
| 05b0 | 100.815611 | 319.526654 | 111.866843 |
| 05b1 | 67.321929 | 209.421024 | 71.685586 |
| 05g0 | 170.966906 | 307.711303 | 42.473651 |
| 05g1 | 112.721674 | 201.738533 | 27.082913 |
| 06b0 | -69.368067 | 271.510229 | 211.577327 |
| 06b1 | -44.990798 | 176.892068 | 138.688627 |
| 06g0 | -62.075884 | 201.039392 | 281.268841 |
| 06g1 | -40.497882 | 131.366602 | 183.597442 |
| 06r0 | -142.652582 | 217.415992 | 235.236395 |
| 06r1 | -91.507191 | 142.258046 | 154.02653 |
| 07b0 | -230.079003 | 248.725586 | 90.110432 |
| 07b1 | -149.776164 | 162.349208 | 59.285354 |
| 07g0 | -157.169347 | 273.669437 | 152.865577 |
| 07g1 | -102.810297 | 178.274913 | 99.90721 |
| 07r0 | -221.309595 | 208.132128 | 174.560575 |
| 07r1 | -143.913946 | 136.693585 | 113.192358 |
| 08b0 | -221.803424 | 272.259753 | -6.211636 |
| 08b1 | -145.265284 | 177.386603 | -5.431518 |
| 08g0 | -286.065058 | 202.039195 | 22.349481 |
| 08g1 | -186.739195 | 132.022379 | 12.777212 |
| 08r0 | -267.131596 | 218.237186 | -68.529187 |
| 08r1 | -174.342669 | 142.799217 | -44.887317 |
| 09b0 | -156.021697 | 249.013794 | -196.563499 |
| 09b1 | -102.178395 | 162.542158 | -129.607057 |
| 09g0 | -193.091064 | 274.193977 | -107.861513 |
| 09g1 | -126.245189 | 178.620804 | -72.407209 |
| 09r0 | -233.76343 | 208.723179 | -162.075132 |
| 09r1 | -151.720648 | 137.079894 | -107.340941 |
| 10b0 | -59.86002 | 265.540413 | -211.283452 |
| 10b1 | -37.266445 | 170.683828 | -138.130403 |
| 10g0 | -107.115709 | 195.411046 | -263.484923 |
| 10g1 | -67.551624 | 125.377658 | -171.890066 |
| 10r0 | -14.780749 | 211.288247 | -273.582087 |
| 10r1 | -8.843079 | 135.951011 | -177.933485 |
| 11b0 | 139.50576 | 248.293187 | -214.7189 |
| 11b1 | 92.177176 | 162.07023 | -142.71045 |
| 11g0 | 43.774573 | 273.782889 | -222.595245 |
| 11g1 | 30.393787 | 178.348443 | -147.943848 |
| 11r0 | 82.547348 | 208.112116 | -277.946892 |
| 11r1 | 55.60644 | 136.678799 | -182.914904 |
| 12b0 | 189.557673 | 271.423166 | -131.893026 |
| 12b1 | 126.650568 | 176.832215 | -87.679249 |
| 12g0 | 224.367138 | 201.099538 | -192.877536 |
| 12g1 | 149.247931 | 131.400462 | -126.856679 |
| 12r0 | 262.555991 | 216.95718 | -108.202097 |
| 12r1 | 173.172677 | 141.962719 | -72.902464 |
| 13b0 | 248.094179 | 247.559534 | 60.73448 |
| 13b1 | 164.697399 | 161.585525 | 38.083722 |
| 13g0 | 226.087017 | 273.004214 | -32.777418 |
| 13g1 | 150.636531 | 177.834147 | -22.313548 |
| 13r0 | 290.491689 | 207.143339 | -12.923788 |
| 13r1 | 191.547962 | 136.044524 | -9.088793 |
| 14b0 | 184.866976 | 270.993398 | 133.902029 |
| 14b1 | 123.062284 | 176.549634 | 87.856774 |
| 14g0 | 253.388508 | 200.458924 | 148.251573 |
| 14g1 | 167.153451 | 130.982473 | 97.299166 |
| 14r0 | 184.712077 | 216.62501 | 210.717473 |
| 14r1 | 123.268834 | 141.741193 | 136.712392 |
| 15b0 | 19.678162 | 247.826858 | 249.129275 |
| 15b1 | 15.161931 | 161.758031 | 162.923877 |
| 15g0 | 101.89678 | 272.934167 | 199.270037 |
| 15g1 | 68.311805 | 177.788781 | 130.866711 |
| 15r0 | 102.697705 | 207.155777 | 266.741106 |
| 15r1 | 68.237506 | 136.053739 | 173.915436 |
| Lycca flange | 1.22 | 3563.57 | -2.56 |

# Text boxes

Magnet

downstreamdet

Tpc3

hcollimator

Vertfoil

Lead Wall

Tpc5

upstreamdet

vcollimator

absorber

Window

LabrDET9

LaBrDET10

BaFDET2

BaFDET3

BaFDET1

BaFDET4

LabrDET8

LabrDET7

BaFDET7

BaFDET6

LabrDET5

LabrDET6

BaFDET8

BaFDET5

LabrDET4

LabrDET3

LabrDET2

LabrDET1

1

2

3

4

5

6

7

8

9

10

11

12

13

14

15